## Slide 1
Learning-Based Quadruped Locomotion
PPO policy training for Unitree Go1 in NVIDIA Isaac Lab
ECE 489 / ME 446 Final Project
Hayk Soghomonyan and Siqi Pan
Project 1, Approach B
Train a robust quadruped locomotion policy that tracks commanded velocity on flat and challenging terrain.
Go1
robot model
12 actuated leg joints
PPO
learning method
RSL-RL in Isaac Lab
2
demo conditions
flat and rough terrain
Demo order: flat policy rollout, then rough-terrain policy rollout.
ECE 489 / ME 446 Final Project | Learning-Based Quadruped Locomotion
01

## Slide 2
PROJECT SCOPE
We implemented the learning-based locomotion track
The final demo focuses on the core quadruped objective from our proposal: stable Go1 locomotion in simulation.
Original proposal objective
Use NVIDIA Isaac Lab for GPU-parallel RL simulation.
Train Unitree Go1 with PPO for velocity tracking.
Evaluate behavior on flat and challenging terrain.
Use domain randomization and terrain curriculum for robustness.
Delivered in final demo
800
flat iterations
final checkpoint model_799.pt
1500
rough iterations
final checkpoint model_1499.pt
Final scope stayed with the core objective: quadruped locomotion under both flat and challenging terrain conditions.
Sources: project proposal and final project requirements
02

## Slide 3
RL FORMULATION
Policy maps observations to joint targets
The high-level policy outputs desired joint positions for the Go1 low-level PD controller.
Observations
base motion, gravity, joint states, previous action, velocity command, and rough-terrain height scan
Policy network
PPO actor-critic MLP. The rough policy keeps terrain context; the flat policy removes it.
Actions
12 joint-position targets, one for each Go1 leg motor.
Simulation
Parallel Isaac Lab environments update contacts, rewards, resets, and terrain.
Reward objective
Track commanded velocity while staying upright, avoiding body contact, limiting effort, and encouraging useful foot swing.
ECE 489 / ME 446 Final Project | Learning-Based Quadruped Locomotion
03

## Slide 4
IMPLEMENTATION
We built a simulation-to-training pipeline in Isaac Lab
The workflow converts the project objective into repeatable flat and rough terrain PPO experiments.
Robot and terrain
Unitree Go1 is simulated under two conditions: a flat plane and generated rough terrain.
Observation and reward
The policy observes robot motion, joint state, commands, and rough-terrain height scan. Rewards encourage velocity tracking and safe contacts.
Parallel PPO training
Thousands of simulated rollouts run on GPU, and RSL-RL updates the actor-critic policy from reward feedback.
Evaluation outputs
The final artifacts are policy checkpoints, TensorBoard curves, and recorded rollout videos for the demo.
Why this matters: one PPO pipeline supports a consistent flat-vs-rough comparison.
ECE 489 / ME 446 Final Project | Learning-Based Quadruped Locomotion
04

## Slide 5
TRAINING SETUP
Flat and rough policies were trained separately
The two-task setup gives a clean comparison between baseline walking and terrain-aware walking.
1024
parallel envs
used for training
cuda:0
GPU device
RTX 4060 laptop GPU
42
random seed
same seed for final runs
video
rollout record
headless video capture
Flat terrain run
Isaac-Velocity-Flat-Unitree-Go1-v0
final checkpoint: model_799.pt
no height scan or terrain curriculum
Rough terrain run
Isaac-Velocity-Rough-Unitree-Go1-v0
final checkpoint: model_1499.pt
height scan and curriculum enabled
ECE 489 / ME 446 Final Project | Learning-Based Quadruped Locomotion
05

## Slide 6
ROBUSTNESS DESIGN
Reward shaping and curriculum improve robustness
Default Isaac Lab reward terms were adjusted to emphasize velocity tracking, regular stepping, and safer contacts.
Domain randomization
friction range
base mass variation
motor strength scaling
observation corruption
Terrain curriculum
begin with easier terrain
increase terrain difficulty
height scan for local terrain
roll out on generated rough terrain
Reward shaping changes
stronger velocity tracking
feet air-time tuned for gait rhythm
torque and acceleration penalties tuned
contact penalties adjusted for stability
Example tuning: linear velocity tracking was increased to 1.5 and yaw tracking to 0.75, while effort and contact penalties constrained unstable motion.
ECE 489 / ME 446 Final Project | Learning-Based Quadruped Locomotion
06

## Slide 7
DEMO CONDITION 1
Flat policy produces stable forward locomotion
The flat task tests the learned gait under a clean plane condition.
Final result video: flat policy after 800 learning iterations.
What to observe
Regular quadruped gait, upright posture, and steady forward progress.
This condition verifies the basic locomotion controller.
ECE 489 / ME 446 Final Project | Learning-Based Quadruped Locomotion
07

## Slide 8
DEMO CONDITION 2
Rough policy traverses generated terrain
The rough task adds elevation changes and terrain height observations.
Final result video: rough policy after 1500 learning iterations.
What to observe
Terrain-aware observations help the policy keep moving over uneven geometry.
Some agents still fail, which shows rough terrain remains the harder condition.
ECE 489 / ME 446 Final Project | Learning-Based Quadruped Locomotion
08

## Slide 9
TRAINING EVIDENCE
Two key curves summarize learning progress
Flat converges higher; rough improves under curriculum but remains lower-return.
Mean reward: flat reaches a higher return plateau.
Mean episode length: flat survives longer and more consistently.
Takeaway: the same PPO pipeline learns both policies, but rough terrain remains the harder condition.
Source: TensorBoard logs from final training runs
09

## Slide 10
EVALUATION
Flat is stable; rough is functional but harder
Last-100 mean TensorBoard scalars from the final flat and rough runs.
Metric
Flat terrain
Rough terrain
Interpretation
Mean reward
30.716
15.883
flat task reaches higher return
Episode length
971.488
808.395
flat policy survives longer
Velocity XY error
0.223
0.392
tracking is harder on rough terrain
Yaw error
0.398
0.444
rough terrain is slightly worse
Base contact termination
0.037
0.315
rough policy has more body contact
Terrain curriculum level
n/a
4.546
rough run progresses through curriculum
Result summary: the flat policy is stable and clean, while the rough policy shows learned traversal with reduced robustness.
ECE 489 / ME 446 Final Project | Learning-Based Quadruped Locomotion
10

## Slide 11
DISCUSSION
Rough-terrain robustness is the main challenge
The final policy satisfies the two-condition demo requirement and shows clear improvement targets.
Strengths
stable flat walking
PPO training pipeline works
rough terrain traversal is visible
reproducible checkpoints and rollout videos
Failure modes
more body contact on rough terrain
weaker velocity tracking
shorter episodes with terrain variation
reward tuning affects posture
Project contributions
custom Go1 task configuration
flat and rough terrain policies
training curves and checkpoints
recorded rollout demo under two conditions
ECE 489 / ME 446 Final Project | Learning-Based Quadruped Locomotion
11

## Slide 12
Conclusion and Demo
We trained PPO policies for Unitree Go1 in Isaac Lab and demonstrated walking under both flat and rough terrain conditions.
flat
stable baseline condition
clean forward gait
rough
challenging condition
terrain-aware traversal
PPO
learning controller
joint-position policy
Go1
robot platform
12-DoF quadruped
Recorded demo order
1. Flat final policy video 2. Rough final policy video
ECE 489 / ME 446 Final Project | Learning-Based Quadruped Locomotion
12

## Slide 13
TECHNICAL BACKUP
Isaac Lab manager terms used in final runs
This backup slide summarizes the active observations, rewards, terminations, and curriculum terms behind the flat and rough policies.
Flat policy MDP
Observation: 48-D policy input
Terrain context: no height scan
Action: 12-D joint position command
Curriculum: none
Rough policy MDP
Observation: 235-D policy input
Terrain context: 187-D height scan
Action: 12-D joint position command
Curriculum: terrain levels enabled
Shared managers
Command: base velocity
Events: friction, mass, motor strength
Push: external push every 10-15 s
Termination: time out and base contact
Key reward weights
velocity tracking: linear 1.5, yaw 0.75
stability penalties: vertical velocity -2.0, roll/pitch angular velocity -0.05
effort penalties: torque -0.0002, acceleration -2.5e-7, action rate -0.01
gait shaping: feet air-time reward
What changed from defaults
linear velocity tracking increased from 1.0 to 1.5
yaw tracking increased from 0.5 to 0.75
flat policy uses stronger orientation and feet air-time shaping
rough policy relies on height scan and terrain curriculum
Technical backup | Isaac Lab manager summaries from final flat and rough runs
13

## Slide 14
Technical Backup: Training and Playback Commands
TRAIN ROUGH TERRAIN
isaaclab.bat -p scripts\reinforcement_learning\rsl_rl\train.py
--task Isaac-Velocity-Rough-Unitree-Go1-v0 --num_envs 1024
--device cuda:0 --max_iterations 1500 --seed 42 --video
--video_length 200 --video_interval 100 --headless
TRAIN FLAT TERRAIN
isaaclab.bat -p scripts\reinforcement_learning\rsl_rl\train.py
--task Isaac-Velocity-Flat-Unitree-Go1-v0 --num_envs 1024
--device cuda:0 --max_iterations 800 --seed 42
--video --headless
PLAY ROUGH TERRAIN
isaaclab.bat -p scripts\reinforcement_learning\rsl_rl\play.py
--task Isaac-Velocity-Rough-Unitree-Go1-v0 --num_envs 512
--device cuda:0 --checkpoint
logs\rsl_rl\unitree_go1_rough\2026-05-25_17-21-50\model_1499.pt
--video --video_length 1000 --enable_cameras --headless
PLAY FLAT TERRAIN
isaaclab.bat -p scripts\reinforcement_learning\rsl_rl\play.py
--task Isaac-Velocity-Flat-Unitree-Go1-v0 --num_envs 512
--device cuda:0 --checkpoint
logs\rsl_rl\unitree_go1_flat\2026-05-25_22-04-58\model_799.pt
--video --video_length 1000 --enable_cameras --headless
TENSORBOARD
tensorboard --logdir=C:\IsaacLab\logs\rsl_rl
Technical backup | Run commands used for final training, playback, and TensorBoard
14

## Slide 15
Technical Backup: Reward Shaping Configuration
The default locomotion reward terms were adjusted to prioritize velocity tracking, stable posture, gait rhythm, and lower effort.
Reward terms in the locomotion MDP: tracking rewards, stability penalties, effort penalties, and foot air-time. (inside velocity environment configuration file)
Final reward overrides used for the tuned runs (rough terrain).
Final reward overrides used for the tuned runs (flat terrain).
Summary: stronger tracking rewards encourage commanded motion; penalties discourage unstable vertical motion, excessive torque, and poor contact behavior.
Technical backup | Reward shaping changes from final configuration
15

## Slide 16
Technical Backup: Reward Shaping Configuration
The default locomotion reward terms were adjusted to prioritize velocity tracking, stable posture, gait rhythm, and lower effort.
PPO configuration
Final reward overrides used for the tuned runs (rough terrain).
Final reward overrides used for the tuned runs (flat terrain).
Technical backup | Reward shaping changes from final configuration
15

## Slide 17
Technical Backup: training details (rough)
The default locomotion reward terms were adjusted to prioritize velocity tracking, stable posture, gait rhythm, and lower effort.
Technical backup | Reward shaping changes from final configuration
15
[INFO] Action Manager: <ActionManager> contains 1 active terms.
+------------------------------------+
| Active Action Terms (shape: 12) |
+--------+-------------+-------------+
| Index | Name | Dimension |
+--------+-------------+-------------+
| 0 | joint_pos | 12 |
+--------+-------------+-------------+
[INFO] Observation Manager: <ObservationManager> contains 1 groups.
+----------------------------------------------------------+
| Active Observation Terms in Group: 'policy' (shape: (235,)) |
+-----------+--------------------------------+-------------+
| Index | Name | Shape |
+-----------+--------------------------------+-------------+
| 0 | base_lin_vel | (3,) |
| 1 | base_ang_vel | (3,) |
| 2 | projected_gravity | (3,) |
| 3 | velocity_commands | (3,) |
| 4 | joint_pos | (12,) |
| 5 | joint_vel | (12,) |
| 6 | actions | (12,) |
| 7 | height_scan | (187,) |
+-----------+--------------------------------+-------------+
[INFO] Termination Manager: <TerminationManager> contains 2 active terms.
+---------------------------------+
| Active Termination Terms |
+-------+--------------+----------+
| Index | Name | Time Out |
+-------+--------------+----------+
| 0 | time_out | True |
| 1 | base_contact | False |
+-------+--------------+----------+
[INFO] Reward Manager: <RewardManager> contains 10 active terms.
+-----------------------------------------+
| Active Reward Terms |
+-------+----------------------+----------+
| Index | Name | Weight |
+-------+----------------------+----------+
| 0 | track_lin_vel_xy_exp | 1.5 |
| 1 | track_ang_vel_z_exp | 0.75 |
| 2 | lin_vel_z_l2 | -2.0 |
| 3 | ang_vel_xy_l2 | -0.05 |
| 4 | dof_torques_l2 | -0.0002 |
| 5 | dof_acc_l2 | -2.5e-07 |
| 6 | action_rate_l2 | -0.01 |
| 7 | feet_air_time | 0.01 |
| 8 | flat_orientation_l2 | 0.0 |
| 9 | dof_pos_limits | 0.0 |
+-------+----------------------+----------+

## Slide 18
Technical Backup: training details (flat)
The default locomotion reward terms were adjusted to prioritize velocity tracking, stable posture, gait rhythm, and lower effort.
Technical backup | Reward shaping changes from final configuration
15
[INFO] Action Manager: <ActionManager> contains 1 active terms.
+------------------------------------+
| Active Action Terms (shape: 12) |
+--------+-------------+-------------+
| Index | Name | Dimension |
+--------+-------------+-------------+
| 0 | joint_pos | 12 |
+--------+-------------+-------------+
[INFO] Observation Manager: <ObservationManager> contains 1 groups.
+---------------------------------------------------------+
| Active Observation Terms in Group: 'policy' (shape: (48,)) |
+-----------+---------------------------------+-----------+
| Index | Name | Shape |
+-----------+---------------------------------+-----------+
| 0 | base_lin_vel | (3,) |
| 1 | base_ang_vel | (3,) |
| 2 | projected_gravity | (3,) |
| 3 | velocity_commands | (3,) |
| 4 | joint_pos | (12,) |
| 5 | joint_vel | (12,) |
| 6 | actions | (12,) |
+-----------+---------------------------------+-----------+
[INFO] Termination Manager: <TerminationManager> contains 2 active terms.
+---------------------------------+
| Active Termination Terms |
+-------+--------------+----------+
| Index | Name | Time Out |
+-------+--------------+----------+
| 0 | time_out | True |
| 1 | base_contact | False |
+-------+--------------+----------+
[INFO] Reward Manager: <RewardManager> contains 10 active terms.
+-----------------------------------------+
| Active Reward Terms |
+-------+----------------------+----------+
| Index | Name | Weight |
+-------+----------------------+----------+
| 0 | track_lin_vel_xy_exp | 1.5 |
| 1 | track_ang_vel_z_exp | 0.75 |
| 2 | lin_vel_z_l2 | -2.0 |
| 3 | ang_vel_xy_l2 | -0.05 |
| 4 | dof_torques_l2 | -0.0002 |
| 5 | dof_acc_l2 | -2.5e-07 |
| 6 | action_rate_l2 | -0.01 |
| 7 | feet_air_time | 0.25 |
| 8 | flat_orientation_l2 | -2.5 |
| 9 | dof_pos_limits | 0.0 |
+-------+----------------------+----------+